## Slide 1: Supply-Voltage Optimization to Account for Process Variations in High-Volume Manufacturing Testing
Gurunath Kadam[1] Markus Rudack[1] Krishnendu Chakrabarty[2] Juergen Alt[1]
[1]Intel Deutschland GmbH, Munich, Germany [2]Duke University, NC, USA

## Slide 2: Objective
Process variation impacts testing
  How to set testing limits?
    How to set the voltage levels on the tester?
Voltage level??
Pass/Fail??

## Slide 3: Outline
Introduction
Related prior work
Proposed method
  Design of Experiments
  Voltage-Level Calculations
Results
Discussion

## Slide 4: Introduction
On-chip process variations: Intra-die vs Inter-die
Intra-die (local) process variations: difficult to predict
Global process variations: easier to model
Foundry A
Foundry B

## Slide 5: Introduction (Contd.)
Problems due to on-chip process variations
  Chip performance difficult to predict
  Testing limits: pessimistic versus relaxed
  Yield loss versus test escape

## Slide 6: Related Prior Work
VDD level manipulation
  Very-Low-Voltage (VLV) to target delay faults [Chang 1996]
  MINVDD: low voltage at-speed testing [Tseng 2001]
  Reduced power-supply voltage to detect gate-oxide failures [Qian 2012]
  Drawback: On-chip process variations not considered
System voltage of individual chip
  Process-window information [Lichtensteiger 2012, IBM]
  Drawback: requires on-chip variable supply, time consuming
Binning
  Speed: Correlation between ring oscillator frequency and transient delay faults [Brand 2004]
  Voltage: Slack time, leakage as function of process variations [Zolotov 2009, IBM]
  Drawback: Speed/Voltage binning is not always desirable

## Slide 7: Proposed Method
Process variation zones on wafer
Process Control Monitoring
  Ring Oscillators (RO)
Test voltage?
Test voltage?
Test voltage?
Notes: Rough RO Length: 41 stages

## Slide 8: Proposed Method (Contd.)
Goal: SPICE parameters emulating on-wafer process variations for each zone
Statistical model to represent process variation zone
  Response of interest: RO output frequency (frequency)
  Variables: process parameters mapped to SPICE parameters
    Frequency, f = ϕ (SPICE parameter1, SPICE parameter2, …)
Notes: SPICE parameters can be varied with precision unlike process parameters.
Toy formulae f = phi(proc para)

## Slide 9: Proposed Method (Contd.)
Obtain SPICE parameters for each zone
  Verify SPICE RO frequency output
Update SPICE models per zones
Find the voltage levels for each zone
  Condition: Maintain required performance
FAST
SLOW
Voltage
Frequency
Nominal
Nominal
Notes: Verification is done by comparing the “normalized” o/p of SPICE RO frequency vs Wafer RO frequency values

## Slide 10: Proposed Method (Contd.)
RO SPICE Models
Desired output response: RO frequency
Monte Carlo simulation of RO SPICE model
Screening for input process parameters
Extract process parameter values zone-wise
Divide wafer map into frequency zones
Build DoE model
Process parameters variation ranges
Create independent RO models for each zone
Find VDD per zone with updated SPICE models
Test devices with new VDD with respect to its location on wafer

## Slide 11: Proposed Method: Design of Experiments
Model quantitative or qualitative effects of variations in input parameters on system output
For m inputs, the output y is modeled as follows:
  Here, xi is the ith input of the system
  β0 is the model constant
  βi is the linear constant and
  βij is the interaction constant
Notes: In above equation, xi is the ith input of the system, while β0 is the model constant, βi is the linear constant and βij is the interaction constant.

## Slide 12: Design of Experiments (Contd.)
Computer simulations, SPICE?
  Time consuming
  Deterministic
  Solution: Design and Analysis of Computer Experiments (DACE)
Space-filling designs
  Represent the whole experimental region
  Observation points spread evenly across the experimental region
  Latin Hypercube Design (LHD)
Notes: Computer simulations: Deterministic: No need for repeated measurements at one observation point

## Slide 13: Design of Experiments (contd.)
0
0.2
0.4
0.6
0.8
1
0.2
0.4
0.6
0.8
1
Input 2
Input 1
0
0.2
0.4
0.6
0.8
1
0.2
0.4
0.6
0.8
1
Input 2
Input 1

## Slide 14: Voltage-Level Calculations
Model construction
  Parameter screening
    To limit the number of runs
    Monte Carlo Simulations: 10000 runs
    Parameter variation range: ±3σ
    Confidence-interval analysis: 10000 runs are sufficient
    Pareto analysis
Dominant parameters
Notes: The number of runs required for the LHD model increase with the number of input parameters.
Screening -> limit # of input parameters -> limit # required runs

## Slide 15: Voltage-Level Calculations (Contd.)
Model construction (Contd.)
  Model building
    Statistical Analysis Software, JMP
    Process parameter variation limit ±3σ
    70 runs provide acceptable value for design discrepancy metric
    Normalization across SPICE and on-wafer frequency values
Notes: Process parameter variation limit ±3σ -> Covers 99.7% of devices
Design discrepancy -> measure of the design space coverage (increases with the # of observation points -> more # runs)

## Slide 16: Voltage-Level Calculations
Model construction (contd.)
  Fitted model with RMSE of 0.0142
  f
Notes: This equation represents the whole wafer area

## Slide 17: Voltage-Level Calculations (Contd.)
Model verification
  SPICE vs LHD
  Quantile-quantile plot
Normalized frequency output from SPICE simulations
Normalized frequency output predicted by LHD model
Notes: First verification between SPICE and LHD models, run-by-run: SPICE vs LHD Predicted

## Slide 18: Voltage Level Calculations (Contd.)
Voltage levels
Where,
Notes: Think?

## Slide 19: Voltage Level Calculations (contd.)
Voltage levels
  pseudo-inverse matrix formulation:
Constraint: is minimum

## Slide 20: Voltage Level Calculations (Contd.)
Voltage levels
  Wafer RO frequency values
  Next find the SPICE parameters for each zone
Zones | Normalized RO frequency
Slow zone | 0.2157
Medium-fast zone | 0.4079
Fast zone | 0.6001

## Slide 21: Voltage-Level Calculations (Contd.)
Voltage levels
  SPICE parameters for each zone
SPICE parameters | Slow zone | Medium-fast zone | Fast zone
vthl_pch | 0.5976 | 0.0357 | -0.5262
l | 0.4561 | 0.0272 | -0.4016
vthl_nch | 0.4667 | 0.0279 | -0.4109
ndop_pch | 0.2626 | 0.0157 | -0.2312
ndop_nch | 0.1787 | 0.0107 | -0.1573
vth0_pch | 0.1484 | 0.0089 | -0.1307
vth0_nch | 0.1156 | 0.0069 | -0.1018
Notes: SPICE parameters after solving fitted model equation for each wafer zone RO frequency values.
Parameter values are normalized between -1 to 1

## Slide 22: Voltage-Level Calculations (Contd.)
Voltage levels
  RO frequency values for updated SPICE models for each zone
  ‘Updated’ SPICE vs On-wafer
Zones | on-Wafer RO frequency (normalized) | Frequency computed using RO SPICE model (normalized) | Error
Slow | 0.2157 | 0.2274 | 5.4%
Medium-fast | 0.4079 | 0.4028 | -1.24%
Fast | 0.6001 | 0.6053 | 0.87%

## Slide 23: Voltage-Level Calculations (Contd.)
Voltage levels
  Voltage sweep to find the nominal frequency output
Zones | Voltage Levels (V)
Slow | 1.06
Medium-fast | 0.99
Fast | 0.92

## Slide 24: Experimental Evaluation
Silicon devices under test
  28nm, from Foundry A
  LTE FDD/TDD slim modem baseband SoC, high-volume
  Main focus: Digital logic
Set-up
  All devices from ‘passed’ bin of previous testing
  Aim: find test escapes
  Ambient temperature
  Screening: performance and leakage tests
  Test patterns are unchanged from previous testing
  Advantest 93K tester
Notes: Main focus: digital logic, , hence the mixed-signal and SRAM testing is not considered

## Slide 25: Results
Pass/Fail | Number of devices |  |  | 
 | Slow zone | Medium-fast zone | Fast zone | Total
Pass | 89 | 80 | 65 | 234
Fail | 0 | 7 | 9 | 16
Total | 89 | 87 | 74 | 250
Fails in zone Medium-fast and Fast
  Failed devices do not match the other devices in that zone

## Slide 26: Results
Scan diagnosis
  Faults at same pins and around the same clock cycle
  Points towards the same subsystem block: Systemic nature
  Further analysis needed!
  Previous one-for-all approach does not work well

## Slide 27: Limitations & Scope for Improvement
Considers only transistor variations
  Interconnects??
LHD model is first-order approximation
  Newer technologies might demand higher-order models
Extend model by adding aging and temperature effects

## Slide 28: Conclusion
Theoretical framework for determining voltage levels for production testing
  Incorporate process variations
  Design of experiments solution (Latin Hypercube Design)
Validated using fabricated devices and on-tester experiments